2. Descriptions of the blocks

hit_left
This block determines whether a cache access is a hit or miss for cache way 0; it does so by combining the functionality of a comparator and an AND gate. It first compares the cache tag with the CPU tag, and then feed the result of comparison and the output from valid array into an AND operation; if the final result is 1, the it is a cache hit, otherwise is a miss.

hit_right
This block works the same as hit_left (i.e. combining comparison and AND operations in one block), but it is for way 1 cache instead of way 0.

lru
The LRU block uses 1 bit to signal which way of the 2 ways is least recently used, and which way should be replaced.

data_selector
This block takes in 128-bit data, and modifies a byte or a word of the data that it takes in based on the value of mem_byte_enable and mem_wdata; finally it passes the output to the data store arrays.

Notes:
1. The block containing tag, index, offset at the top of my diagram doesn't actually exist in the cache datapath; they are just three signals taken from different bits in the address. The block is on the diagram just to facilitate understanding and visualize things.
2. In my diagram, all the write signals in array blocks are not connected to there corresponding load signals; this is to avoid messiness, and it doesn't mean that they are not connected in the actual datapath.

3. Testing strategy

In order to test my MP, I first went to make sure that, having implemented the cache, all register values are still correct when running some test code; in other words, I first did some regression testing to make sure what was working before still works now. To come up with my own test code, I've also studied the test code provided to us. My testing strategy is to mainly use LDR and STR to read from and write to memory addresses. Since we are using a 2-way set associative cache with LRU replacement policy, my focus was more on testing the replacement part. I first filled a particular cache set with two values, and then modify one of the values, and then bring in to the same set a third value so that one of the previous two was replaced by the most recent one, and then I would check whether the memory was updated correctly.

Another thing that I did was to make sure that, having implemented the cache, the memory access time should be much faster compared with when there was no cache. To do this I run my same test code on both my implementation for this MP and the previous MP1 (with no cache in datapath). The result was indeed very good. My testcode finished running within 2300ns on my new implementation, while it took over 8000ns on my MP1. There's also a place in my testcode, where two instructions would result in a cache hit; by examining the wavetrace of that two instructions, I found that the hit time is roughly 70ns, while running on my MP1 the two instructions would take nearly 500ns.

A piece of my sample test code can be found on the next page.

ORIGIN 0
SEGMENT CodeSegment:
    AND R0, R0, 0

    LDR R1, R0, A30
    LDR R2, R0, C30
    ADD R1, R3, 6
    STR R1, R0, A30
    LDR R4, R0, F30
    LDR R1, R0, A30

    LDR R2, R0, A32
    ADD R2, R2, 6
    STR R2, R1, F30
    ADD R3, R3, 3
    STR R4, R0, F30
    LDR R4, R0, F30
    LDR R5, R0, F36
    LDR R6, R0, A32
    LDR R6, R0, A34
    STR R6, R0, A86
    LDR R6, R0, A82

DONE:
    BRnzp DONE

SEGMENT DataSegment:
A30: DATA2 4x110A;
A32: DATA2 4x110A;
A34: DATA2 4x110A;
A36: DATA2 4x110A;
A38: DATA2 4x110A;
A3A: DATA2 4x110A;
A3C: DATA2 4x110A;
A3E: DATA2 4x110A;

A80: DATA2 4x3333;
A82: DATA2 4x3333;
A84: DATA2 4x3333;
A86: DATA2 4x3333;
A88: DATA2 4x3333;
A8A: DATA2 4x3333;
A8C: DATA2 4x3333;
A8E: DATA2 4x3333;

C30: DATA2 4x6666;
C32: DATA2 4x6666;
C34: DATA2 4x6666;
C36: DATA2 4x6666;
C38: DATA2 4x6666;
C3A: DATA2 4x6666;
C3C: DATA2 4x6666;
C3E: DATA2 4x6666;

F30: DATA2 4xBAAD;
F32: DATA2 4xBAAD;
F34: DATA2 4xBAAD;
F36: DATA2 4xBAAD;
F38: DATA2 4xBAAD;
F3A: DATA2 4xBAAD;
F3C: DATA2 4xBAAD;
F3E: DATA2 4xBAAD;